## Slide 1: KalmanNet: Neural Network Aided Kalman Filtering for Partially Known Dynamics
G. Revach, N. Shlezinger, X. Ni, A. L. Escoriza,R. J. G. van Sloun, Y. C. Eldar
Presented by Spencer J. Chang & Zhenjiang Mao

## Slide 2: Dynamical System State Estimation
Roboflow Blog
MathWorks
Notes: Estimating the state of systems that evolve over time is a fundamental task in signal processing and control, but these states are often hidden from our view or may not be directly measured by us with sensors. Some applications include localization, tracking, navigation.
For a more tangible set of examples, consider that any sensor we may use in the real-world is going to be noisy and could have a thin or wide range of measurement values.
So, then how do we estimate the true value of a measurement? One way is to take measurements across time and to estimate the true state of the sensor by comparing our predictions to those measurements.
Extra:
It could also be a system that a user is trying to model but the state of the system may not be directly measurable.
Consider the measurement of a rocket thruster’s output. This cannot be done by putting a sensor inside the thruster; it must be placed in a cooler location.

## Slide 3: Measurements Across Time
https://github.com/rlabbe/Kalman-and-Bayesian-Filters-in-Python/
Hypothesis: +1 lb / day
Notes: Unclear figures. I can guess this is about weigts prediction. Maybe we can add more information like 'weight prediction' so that people can read it easily.

## Slide 4: Measurements Across Time
https://github.com/rlabbe/Kalman-and-Bayesian-Filters-in-Python/
Initial Hypothesis: -1 lb / day
Constant Gain
Initial Hypothesis: -1 lb / day
Adaptive Gain

## Slide 5: G-h Filters and the Kalman Filter (KF)
Mathworks – “Kalman Filtering”
Notes: The Kalman Filter (KF) has been used to estimate such state spaces by assuming a model of the internal state transitions and state to observation transitions as linear functions.
Shortly after its introduction, the Extended Kalman Filter was published and enables the KF to solve nonlinear state estimation problems in time-varying systems.
Other variations include the “Unscented KF” and the Particle Filter.

## Slide 6
N. Shlezinger, J. Whang, Y. C. Eldar, and A. G. Dimakis, “Model-based deep learning,” arXiv [eess.SP], 15-Dec-2020.
Mamba (S4M)
KalmanNet
Kalman Filter
RNNs, LSTMs
Notes: There are still problems with using a model-based state estimation filter like the KF, EKF, UKF, PF.
  Assumes a model on the state transitions typically based on knowledge of sensors or environment knowledge.
Prerequisites of both
  MB: domain knowledge, full parameterization
  DD: Lots of data and lots of trainable parameters
KalmanNet: DNN-aided model. The model is enhanced by including a network at a component in the overall state estimation process.
S4: Model-aided DNN. We use a structured state-space model to enable the network to understand long-range dependencies.

## Slide 7: Methodology

## Slide 8: System Estimation Pipeline
LTI
KF
LTV
NL
KN
LTI System
KF Solution
LTV System
Nonlinearities
KalmanNet

## Slide 9: LTI System Example
https://www.mathworks.com/help/control/ug/kalman-filtering.html
LTI
KF
LTV
NL
KN
Notes: System Equations here to help explain the sizes of A, B, C, D and how x(t) and y(t) relate to each other.

## Slide 10: LTI System Output
LTI
KF
LTV
NL
KN

## Slide 11: KF Solution
LTI
KF
LTV
NL
KN
Notes: Prediction Equations
  Placeholder text
Update Equations
  Placeholder text
How are parameters updated? What parameters are updated?

## Slide 12: KF Solution
State Estimate
Update (a posteriori)
Predict (a priori)
LTI
KF
LTV
NL
KN
Notes: Prediction Equations
  Placeholder text
Update Equations
  Placeholder text
How are parameters updated? What parameters are updated?

## Slide 13: KF Approximation of LTI System
LTI
KF
LTV
NL
KN

## Slide 14: LTV System Example
LTI
KF
LTV
NL
KN

## Slide 15: LTV System Output
LTI
KF
LTV
NL
KN

## Slide 16: KF Approximation of LTV System
More Prediction Influence (f = 1)
Less Prediction Influence (f = 0.75)
LTI
KF
LTV
NL
KN

## Slide 17: Extended Kalman Filter (EKF)
LTI
KF
LTV
NL
KN

## Slide 18: EKF Diagram + Issues
LTI
KF
LTV
NL
KN
Notes: Need full knowledge of underlying model to be optimal
  Underlying noise statistics
  Degradation during model mismatches
Linearization may not be able to keep up
  Severe nonlinearities

## Slide 19: KalmanNet Diagram
LTI
KF
LTV
NL
KN

## Slide 20: KalmanNet Input Options
LTI
KF
LTV
NL
KN
F1 – Observation
F2 – Innovation
F3 – Forward Evolution
F4 – Forward Update
Notes: Good combos: (F1, F2, F4) and (F1, F3, F4).

## Slide 21: KalmanNet Architecture #1
LTI
KF
LTV
NL
KN
F4 – Forward Update
F2 – Innovation

## Slide 22: Arch. #2
LTI
KF
LTV
NL
KN

## Slide 23: KalmanNet Training
Training Algorithm （Back Propagation Through Time：BPTT)

## Slide 24: Squared-error loss
loss gradient
MSE on all trajectory

## Slide 25: Experimental Results
Experiments with Linear State Space Models
Experiments with Nonlinear State Space Models
Localization Experiments with Real Data

## Slide 26: Experiment Settings
F1 – Observation
F2 – Innovation
F3 – Forward Evolution
F4 – Forward Update

## Slide 27: I: Experiments with Linear State Space Models
setting C1
C1 | #1 | {F2, F4} | V3
C2 | #1 | {F2, F4} | V1
C3 | #1 | {F1, F3, F4} | V2
C4 | #2 | All features | V1
C: configuration
#: architecture
F: Input type
V: Algorithm

## Slide 28: II: Experiments with Nonlinear State Space Models​
State-Evolution Mismatch
Partial Information
ii. State-Observation Mismatch
setting C4
Use a rotated observation matrix Hα=10◦ for data generation (H = I is the original one)
C1 | #1 | {F2, F4} | V3
C2 | #1 | {F2, F4} | V1
C3 | #1 | {F1, F3, F4} | V2
C4 | #2 | All features | V1

## Slide 30: Lorenz Attractor (Full Information)
Lorenz attractor: a 3d chaotic system, which is composed of the solution of the continuous-time Lorenz system differential equation and is used to simulate nonlinear and chaotic trajectories.
setting C4
h(x_t) = xt+ noise​
C1 | #1 | {F2, F4} | V3
C2 | #1 | {F2, F4} | V1
C3 | #1 | {F1, F3, F4} | V2
C4 | #2 | All features | V1

## Slide 32: Lorenz Attractor (Partial Information)
setting C4

## Slide 34: Real World Dynamics: NCLT
Michigan NCLT Dataset ( North Campus Long-Term Vision and Lidar Dataset): perception and localization tasks for mobile robots in different environments and conditions

## Slide 35: Implement Archtecture#1 on S&P500 Prediction

## Slide 36: Conclusions
Overview:
Combines deep learning with the classic model-based (MB) Extended Kalman Filter (EKF).
Uses a Recurrent Neural Network (RNN) to improve EKF’s performance in complex environments.
Design Details:
Replaces EKF’s model-dependent computations with a dedicated RNN.
The RNN operates on specific features containing essential information for state estimation.
Learns to handle model mismatches and non-linearities during estimation.

## Slide 37: Advantages
Performance:
Provides real-time state estimation comparable to MB Kalman filtering.
Successfully addresses model mismatches and non-linearities, which are challenging for traditional EKF.
Efficiency:
Utilizes a compact RNN, requiring a small training dataset.
Has reduced computational complexity, suitable for high-dimensional models and resource-limited devices.

## Slide 38: Disadvantages
Scalability and over-parameterization:
The paper mentions that GRUs can lead to "severe over-parameterization" when tracking high-dimensional state spaces. Although the authors propose using independent GRUs to alleviate this problem, this approach may still face challenges when facing larger and more complex systems.
Model interpretability and flexibility:
Since KalmanNet combines RNN and Kalman filter updates, it improves flexibility but also introduces additional complexity, which may affect the interpretability of the model.

## Slide 39: Disadvantages
Limitations of hyperparameter tuning:
The study relied on hyperparameter tuning (e.g., optimizing the covariance matrix via grid search) to achieve optimal performance. However, the computational cost and stability challenges of these parameter tuning were not discussed in detail in the paper.
Sensitivity to data quality and quantity:
Although the model was trained on relatively short trajectories and validated on a variety of tasks, it is unclear how KalmanNet will perform with limited data (e.g., fewer labeled samples or shorter trajectories).

## Slide 40: Disadvantages
Training efficiency and computational cost:
KalmanNet uses the Back Propagation Through Time (BPTT) algorithm for training, which may be computationally intensive when the trajectories are long or the dependencies are complex.
Limited comparison with other hybrid models:
The paper mainly compares KalmanNet with standard MB filters and end-to-end RNN models. However, it would be helpful to compare it with other hybrid methods or neural networks designed for state estimation (e.g., variants based on UKF or PF).

## Slide 42: Acknowledgements
Ritesh – Flow of slide deck
Dr. Stokes – Kalman Filter Discussions

## Slide 43: Dynamical Systems
Dr. Eric Weeks, Emory University
Roboflow Blog
Notes: Estimating the state of systems that evolve over time is a fundamental task in signal processing and control, but these states are often hidden from our view or may not be directly measured by us with sensors. Some applications include localization, tracking, navigation.
For a more tangible set of examples, consider that any sensor we may use in the real-world is going to be noisy and could have a thin or wide range of measurement values.
So, then how do we estimate the true value of a measurement? One way is to take measurements across time and to estimate the true state of the sensor by comparing our predictions to those measurements.
Extra:
It could also be a system that a user is trying to model but the state of the system may not be directly measurable.
Consider the measurement of a rocket thruster’s output. This cannot be done by putting a sensor inside the thruster; it must be placed in a cooler location.

## Slide 44: Problems & Solutions
Time-varying system
State estimation
Enter the “Kalman Filter” (KF) – linear estimator
  Other problems: Nonlinearities  Solutions: Extended KF, Unscented KF, Particle Filter  Other problems: Mismatched models
Need image(s) here to get the point across

## Slide 45: KF Solution
Notes: Prediction Equations
  Placeholder text
Update Equations
  Placeholder text
How are parameters updated? What parameters are updated?

## Slide 46: Review: Jacobian Matrix
LTI
KF
LTV
NL
KN
Example – Polar-Cartesian Conversion